# Series

OTH4000-GT 	Wireless Communication Programmable 
Electronic Thermostat

# Features

# Remote access requires an Internet connection 
and a GT125 Web interface (not included).

Type	-  Wireless communication programmable electronic

proportional pulsing line voltage thermostat.

- Transmitter module: 
IC: 7693A-89XAM9A
FCC ID: OA3MRF89XAM9

Color	-	Standard: white.

Voltage	-	120/208/240V, 50/60 Hz.

Rating	-	Maximum load: 16.7A at 120/208/240V.

-	Minimum load: 0.5A at 120/208/240V.

Control	-	10-minute cycle (forced-air heater) or 15-second cycle (convector).

-	Resolution: 0.5 °C (1 °F).

-	Precision: ± 0.15 °C (0.27 °F) on 15-second cycle.

-	Precision: ± 0.5 °C (0.1 °F) on 10-minute cycle.

Temperature range	-	5 °C (41 °F) to 30 °C (86 °F).

Display	-	Digital screen with white LED backlit.

-	Display forced-air heater mode and keypad lock (when activated).

-		Temperature display format (°C or °F) and time format (24h or 12h).

Programming features are accessible only through the neviweb® Web platform. Connection requires a GT125 interface.

Installation	-	2-wire thermostat, easy to install.

Application	-	Baseboard heater, radiant ceiling, convector and forced-air convector.

Warranty	-	5-year warranty against defects.

# Model

| Product # | Description | Volts | Watts | Qty |
| --- | --- | --- | --- | --- |
| OTH4000-GT1 | Wireless communication programmable electronic proportional pulsing line voltage thermostat | 120/208/240 | 2000/3465/4000 |  |
| GT1252 | Web interface that provides remote access to all your neviweb®–compatible products | - | - |  |

1 Standard color is white.

2 Standard color is black.

# Specifications may change without prior notice

| Project: | Approval Information |
| --- | --- |
| Consultant Engineer: |  |
| Electrician Contractor: |  |
| Distributor: |  |
| Date: |  |
| Contact in Ouellet: |  |
| Comments: |

# Text boxes

Neviweb® is a registered trademark

of Sinopé Technologies Inc.

in Canada and the United States.

CSA-C828-06

Performance Standard