Series

OAV	Vertical Unit Heater

Features

Color	-	Standard: almond.

Finish	-	Standard: epoxy/polyester powder paint.

Voltage	-	208V, 240V, 347V, 480V, 600V, 1 or 3-phase.

Construction	-	18-gauge steel.

-	Linear high-limit temperature control with automatic reset.

-	Terminal block for remote fan control.

Fan	-	Fan delay; keeps the fan stopped at the beginning to let the heating elements

warm-up and keeps the fan going when the heater is stopped to purge

heater of residual heat.

-	Totally enclosed, ball-bearing motor.

-	Motor is thermally protected.

Heating element	-	Finned tubular heating elements grounded for extra safety.

Control	-	All models have factory installed contactor.

-	240V control circuit (with transformer if necessary).

-	24V relay, with or  without transformer available.

-	120V control circuit available.

-	30 °C (85 °F) maximum operating ambient temperature.

Any remote thermostat or relay must be connected to the heater control terminal block.

Installation	-	Mounting for 10kW and less: 4 threaded holes (1/2 in. - 13 UNC).

- Mounting for 15kW or more: 4 hooks.

- Cones available upon request.

Warranty	-	3-year warranty against defects.

Application 	-	Factory, warehouse, commercial building, garage.

Models

| Product# | Qty | Volts (ph) | kW | BTU/hr | cfm | Temperature Rise | Motor | Weight |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  | oC | oF | HP | rpm | lb | kg |
| OAV05008AM |  | 208 (1) | 5.0 | 17060 | 450 | 19 | 34 | 1/25 | 1050 | 75 | 34 |
| OAV05038AM |  | 208 (3) | 5.0 | 17060 | 450 | 19 | 34 | 1/25 | 1050 | 75 | 34 |
| OAV07538AM |  | 208 (3) | 7.5 | 25590 | 600 | 22 | 40 | 1/25 | 1050 | 75 | 34 |
| OAV10038AM |  | 208 (3) | 10.0 | 34120 | 750 | 23 | 42 | 1/25 | 1050 | 75 | 34 |
| OAV15038AM |  | 208 (3) | 15.0 | 51180 | 1200 | 22 | 40 | 1/6 | 1075 | 100 | 48 |
| OAV20038AM |  | 208 (3) | 20.0 | 68240 | 1600 | 22 | 40 | 1/6 | 1075 | 100 | 48 |
| OAV25038AM |  | 208 (3) | 25.0 | 85300 | 2000 | 22 | 40 | 1/6 | 1075 | 100 | 48 |
| OAV30038AM |  | 208 (3) | 30.0 | 102360 | 2300 | 23 | 41 | 1/6 | 1075 | 100 | 48 |
| OAV05000AM |  | 240 (1) | 5.0 | 17060 | 450 | 19 | 34 | 1/25 | 1050 | 75 | 34 |
| OAV07500AM |  | 240 (1) | 7.5 | 25590 | 600 | 22 | 40 | 1/25 | 1050 | 75 | 34 |
| OAV10000AM |  | 240 (1) | 10.0 | 34120 | 750 | 23 | 42 | 1/25 | 1050 | 75 | 34 |
| OAV15000AM |  | 240 (1) | 15.0 | 51180 | 1200 | 22 | 40 | 1/6 | 1075 | 100 | 48 |
| OAV20000AM |  | 240 (1) | 20.0 | 68240 | 1600 | 22 | 40 | 1/6 | 1075 | 100 | 48 |
| OAV25000AM |  | 240 (1) | 25.0 | 85300 | 2000 | 22 | 40 | 1/6 | 1075 | 100 | 48 |
| OAV30000AM |  | 240 (1) | 30.0 | 102360 | 2300 | 23 | 41 | 1/6 | 1075 | 100 | 48 |
| OAV05007AM |  | 347 (1) | 5.0 | 17060 | 450 | 19 | 34 | 1/25 | 1050 | 75 | 34 |
| OAV07507AM |  | 347 (1) | 7.5 | 25590 | 600 | 22 | 40 | 1/25 | 1050 | 75 | 34 |
| OAV10007AM |  | 347 (1) | 10.0 | 34120 | 750 | 23 | 42 | 1/25 | 1050 | 75 | 34 |
| OAV25034AM |  | 480 (3) | 25.0 | 85300 | 2000 | 22 | 40 | 1/6 | 1075 | 100 | 48 |
| OAV30034AM |  | 480 (3) | 30.0 | 102360 | 2300 | 23 | 41 | 1/6 | 1075 | 100 | 48 |
| OAV05006AM |  | 600 (1) | 5.0 | 17060 | 450 | 19 | 34 | 1/25 | 1050 | 75 | 34 |
| OAV05036AM |  | 600 (3) | 5.0 | 17060 | 450 | 19 | 34 | 1/25 | 1050 | 75 | 34 |
| OAV07536AM |  | 600 (3) | 7.5 | 25590 | 600 | 22 | 40 | 1/25 | 1050 | 75 | 34 |
| OAV10036AM |  | 600 (3) | 10.0 | 34120 | 750 | 23 | 42 | 1/25 | 1050 | 75 | 34 |
| OAV15036AM |  | 600 (3) | 15.0 | 51180 | 1200 | 22 | 40 | 1/6 | 1075 | 100 | 48 |
| OAV20036AM |  | 600 (3) | 20.0 | 68240 | 1600 | 22 | 40 | 1/6 | 1075 | 100 | 48 |
| OAV25036AM |  | 600 (3) | 25.0 | 85300 | 2000 | 22 | 40 | 1/6 | 1075 | 100 | 48 |
| OAV30036AM |  | 600 (3) | 30.0 | 102360 | 2300 | 23 | 41 | 1/6 | 1075 | 100 | 48 |
| OAV40036AM |  | 600 (3) | 40.0 | 136480 | 4800 | 15 | 26 | 3/4 | 1140 | 215 | 98 |
| OAV50036AM |  | 600 (3) | 50.0 | 170600 | 4800 | 18 | 33 | 3/4 | 1140 | 215 | 98 |
| OAV60036AM |  | 600 (3) | 60.0 | 204720 | 4800 | 22 | 40 | 3/4 | 1140 | 215 | 98 |

Options

| Product # Kit | Product # Factory installed* | Description | Qty |
| --- | --- | --- | --- |
| - | 120 | 120V control circuit |  |
| - | 3P | Triple-pole contactor |  |
| KIT-OAV-CJ-1AM | - | Jet cone, 5 to 10kW units |  |
| KIT-OAV-CJ-2AM | - | Jet cone, 15 to 30kW units |  |
| KIT-OAV-CJ-3AM | - | Jet cone, 40 to 60kW units |  |
| KIT-OAV-CS-1AM | - | Single cone, 5 to 10kW units |  |
| KIT-OAV-CS-2AM | - | Single cone, 15 to 30kW units |  |
| KIT-OAV-CS-3AM | - | Single cone, 40 to 60kW units |  |
| KIT-OAV-CT-1AM | - | Triple cone, 5 to 10kW units |  |
| KIT-OAV-CT-2AM | - | Triple cone, 15 to 30kW units |  |
| KIT-OAV-CT-3AM | - | Triple cone, 40 to 60kW units |  |
| - | DIS40 | Disconnect switch, triple-pole, 40A at 600V |  |
| - | DIS80 | Disconnect switch, triple-pole, 80A at 600V |  |
| - | DIS100 | Disconnect switch, triple-pole, 100A at 600V |  |
| KIT-OAV-R | R | 24V relay, without transformer |  |
| KIT-OAV-RT | RT | 24V relay, with transformer |  |

* For factory installed options, add the option number to the product number. See the Product Code section inside the front cover.

Standard color is almond.

### Others

| Type | Quantity | Model et description Complementary informations | Volts | Phase | Watts | Length mm/in. | Informations Color/installation |
| --- | --- | --- | --- | --- | --- | --- | --- |

Specifications may change without prior notice

| Project: | Approval Information |
| --- | --- |
| Consultant Engineer: |  |
| Electrician Contractor: |  |
| Distributor: |  |
| Date: |  |
| Contact in Ouellet: |  |
| Comments: |