# Series

OFE-C	Comfort Electric Furnace

Features

Finish	-	Non-painted galvanized steel.

Voltage	-	240/208V, 1-phase.

Construction	-	Robust galvanized steel casing, all insulated for reduced heat loss and noise.

-	One panel on casing provides access to internal parts.

Fan	-	High quality precision balanced blower for quiet operation and optimal performance.

Motor	-	Standard motor (PSC), permanently lubricated and rubber mounted for maximum vibration and noise reduction.

-	Relay and printed circuit board (PCB) control automatic operation of motor and allow for the addition of air conditioning or heat pump.

Heating element	-	Heavy duty, reliable 4kW and 5kW Helical coil nickel-chromium alloy wire provide superior heat transfer with unrestricted air flow.

- Heating elements can be individually replaced.

- High-limit temperature control with automatic reset.

- Elements modulation is done by a low voltage printed circuit board to prevent power surges.

Control	-	Heavy duty 24VAC transformer provides power to relays and controls.

-	Built-in breakers with manual reset.

-	Compatible with 1 or 2-stage thermostat with or without external unit.

-	A 120V terminal block also permits installation of accessories such as humidifier and electronic filter (maximum 2A).

Installation	-	Multi-position installation, sides, back, or bottom air returns.

- Approved for zero clearance installation against combustible surfaces.

Warranty	-	5-year warranty against defects.

Application	-	For cottages, homes or offices, also approved for mobile homes use. May be installed in a basement, closet, crawl space or any unused area or alcove.

# Models with Standard Motor (PSC)1

| Product # | Volts (1 ph) 2 wires | kW (BTU/hr) | Amp including motor | Motor HP | Static Pressure at 0.5" W.C. | Weight | Qty |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  | Motor Speed2 | cfm3 | lb | kg |  |
| OFEC10000 | 240/208 | 10.0 (34120) / 7.5 (25628) | 44.0 / 38.2 | 1/3 | Low | 595 | 105 | 48 |  |
| OFEC15000 | 240/208 | 15.0 (51180) / 11.3 (38442) | 64.7 / 56.1 | 1/3 | Low | 595 | 105 | 48 |  |
| OFEC18000 | 240/208 | 18.0 (61420) / 13.5 (46130) | 78.4 / 68.0 | 1/3 | Low | 595 | 105 | 48 |  |
| OFEC20000 | 240/208 | 20.0 (68240) / 15.0 (51256) | 85.4 / 74.1 | 1/3 | Low | 595 | 105 | 48 |  |

# Options

| Product # Kit | Description | Qty |
| --- | --- | --- |
| OFE-SO2 | Downflow base |  |
| OFE-AK2 | Adaptor kit for 17 in. x 17 in. duct |  |

1 Installation is forbidden outside Québec.

2 Factory settings.

3 Refer to the installation instructions and owner’s manual for complete air flow tables.

Wall Controls

Compatible with any low voltage thermostat.

# Specifications may change without prior notice

| Project: | Approval Information |
| --- | --- |
| Consultant Engineer: |  |
| Electrician Contractor: |  |
| Distributor: |  |
| Date: |  |
| Contact in Ouellet: |  |
| Comments: |