# Series

OSR		Controller options for pipe tracing for use in non-hazardous (ordinary) and hazardous locations

|  | Product # | DescrIption | Qté |
| --- | --- | --- | --- |
|  | TXR-L2S-10-Q101 | SPDT, explosion-proof, NEMA 4, 7 and 9 thermostat. Anodized aluminum housing. 22A at 120/250/480V. 10 ft. (3 m) stainless steel bulb and capillary. Ambient temperature: -40°F to 140°F (-40°C to 60°C). |  |
|  | TM-1SIH1-E5-RTD-A1 | TraceMateTM I GFCI electronic thermostat. NEMA 4X. Class I, Division 2 / Zone II areas. Single circuit at 120V. 100-ohm, 3-wire platinum RTD. Ambient temperature: -58°F to 932°F (-50°C to 500°C). |  |
|  | TM-1DIH2-E5-RTD-A1 | TraceMateTM I GFCI electronic thermostat. NEMA 4X. Class I, Division 2 / Zone II areas. Single circuit at 240/208V. 100-ohm, 3-wire platinum RTD. Ambient temperature: -58°F to 932°F (-50°C to 500°C). |  |
|  | TM-2SIH1-E5-RTD | TraceMateTM I GFCI electronic thermostat. NEMA 4X. Class I, Division 2 / Zone II areas. Dual circuit at 120V. 100-ohm, 3-wire platinum RTD. Ambient temperature: -58°F to 932°F (-50°C to 500°C). |  |
|  | TM-2DIH2-E5-RTD | TraceMateTM I GFCI electronic thermostat. NEMA 4X. Class I, Division 2 / Zone II areas. Dual circuit at 240/208V. 100-ohm, 3-wire platinum RTD. Ambient temperature: -58°F to 932°F (-50°C to 500°C). |  |
|  | MS-21012 | MasterTrace electronic GFCI controller with user interface. NEMA 4X. Class I, Division 2 / Zone II areas. Single circuit double pole. 30A to 85V-280V. RS485 type communication, Modbus® RTU protocol. Ambiant temperature: -58°F to 932°F (-50°C to 500°C). |  |
|  | MS-21022 | MasterTrace electronic GFCI controller with user interface. NEMA 4X. Class I, Division 2 / Zone II areas. Double circuit single pole. 30A to 120 or 277V. RS485 type communication, Modbus® RTU protocol. Ambient temperature: -58°F to 932°F (-50°C to 500°C). |  |
|  | RTD-7 | RTD probe for MasterTrace controller. |  |

1 Requires a ground fault circuit interrupter (GFCI) in the electrical panel.

2 Requires a RTD probe for MasterTrace controller (RTD-7).

Specifications may change without prior notice

| Project: | Approval Information |
| --- | --- |
| Consultant Engineer: |  |
| Electrician Contractor: |  |
| Distributor: |  |
| Date: |  |
| Contact in Ouellet: |  |
| Comments: |