Series

OVE	European-Style Bathroom Fan Heater

Features

Color	-	Standard: white, almond.

- Optional (upcharge applicable): metallic silver, bronze, metallic charcoal,

aluminum, semi-gloss black, sand.

-	Custom color available upon request.

Finish	-	Standard: epoxy/polyester powder paint.

-	Optional: stainless steel (grilles and back of the heater are painted black).

Voltage	-	120V, 240/208V, 1-phase.

Construction	-	20-gauge steel or 22-gauge stainless steel.

-	Outlet-grille efficiently distributes warm air throughout the heated area.

-	Bar grilles prevent insertion of foreign objects; 
smooth-finish paint is washable and anti-yellowing.

-	High-limit temperature control with automatic reset.

Fan	-	Whisper-quiet squirrel-cage fan.

-	Factory-lubricated motor.

Heating element	-	Nickel-chromium alloy stitched wire protected by mica insulators.

-	Heating element provides instant heat.

Control	-	Bulb thermostat (-T and -TM models).

-	Mechanical timer, 0-60 minutes (-TM model).

Note: If an electronic wall-mounted thermostat is used, it must be compatible with forced-air heaters.

Installation	-	12 in. (306 mm) minimum clearance to ﬂoor.

-	May be recessed or surface-mounted without adaptor in 2 in. X 3 in. stud partitions.

-	Holes for fastening and convenient knock-outs allow for easy installation 
and connection (mounting screws included).

Warranty	-	5-year warranty against defects.

Application	-	Bathroom, kitchen, family room, entrance way.

Models

| # Product | Qty | Volts | Watts | Weight |
| --- | --- | --- | --- | --- |
|  |  |  |  | lb | kg |
| OVE15021 |  | 120 | 1500 | 14.0 | 6.4 |
| OVE1502-T |  | 120 | 1500 | 14.0 | 6.4 |
| OVE1502-TM |  | 120 | 1500 | 14.0 | 6.4 |
| OVE15001 |  | 240/208 | 1500/1125 | 14.0 | 6.4 |
| OVE1500-T |  | 240/208 | 1500/1125 | 14.0 | 6.4 |
| OVE1500-TM2 |  | 240/208 | 1500/1125 | 14.0 | 6.4 |
| OVE1500BL-TM3 |  | 240/208 | 1500/1125 | 14.0 | 6.4 |

1 Requires non pulsing wall-mounted thermostat. Please refer to the Wall Thermostats Reference Chart at the end of the catalog.

2 Price for standard “AM” almond color and base price for upcharge applicable on optional colors.

3 Price for standard “BL” white color.

Add "BL" for white, "AM" for almond, "SS" for stainless steel.

For almond models with -T or -TM the knobs are black.

For stainless steel models the grilles and the back of the heater are painted black.

### Others

| Type | Quantity | Model et description Complementary informations | Volts | Phase | Watts | Length mm/in. | Informations Color/installation |
| --- | --- | --- | --- | --- | --- | --- | --- |

Specifications may change without prior notice

| Project: | Approval Information |
| --- | --- |
| Consultant Engineer: |  |
| Eectrician Contractor: |  |
| Distributor: |  |
| Date: |  |
| Contact in Ouellet: |  |
| Comments: |