Series

OEC	Executive Convector

Features

Color	-	Standard: white, almond, metallic silver, bronze, metallic charcoal,

aluminum, semi-gloss black, sand.

-	Custom colors available upon request.

Finish	-	Standard: epoxy-polyester powder paint.

-	Optional: stainless steel (grilles are painted black).

Voltage	-	347V, 1-phase.

Construction	-	20-gauge steel or 22-gauge stainless steel.

-	Warm air outlet that directs the air to the center of the room.

-	High-limit temperature control with automatic reset.

-	Bar grilles prevent insertion of foreign objects; smooth-ﬁnish paint is washable.

Heating element	-	Quiet monoblock element.

Watt density	-	700W/ft. (2320W/m).

Control	-	Wall-mounted electronic thermostat (-OTH models)

or built-in electronic relay (-TRIAC and -TRIACT models).

Installation	-	2 in. (51 mm) minimum clearance to ﬂoor.

-	Not for residential use.

-	The convector’s wall mounting bracket is connected to a power supply.

-	Simply place the convector on the bracket to make it operational.

Warranty	-	5-year warranty against defects.

(The warranty is valid only if the heater is controlled with an electronic proportional

pulsing thermostat with a cycle of 15 seconds maximum or a built-in 24V electronic relay and the junction box must be fixed to the wall with the anchor supplied.)

Application	-	Office building, apartment building, condo.

Models

| Product # Without thermostat | Qty | Product # Non programmable Wall-Mounted Thermostat included | Qty | Volts | Watts | Length |
| --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  | in. | in. |
| OEC0757 |  | OEC0757-OTH |  | 347 | 750 | 16 1/2 | 418 |
| OEC1007 |  | OEC1007-OTH |  | 347 | 1000 | 19 7/16 | 492 |
| OEC1257 |  | OEC1257-OTH |  | 347 | 1250 | 23 | 584 |
| OEC1507 |  | OEC1507-OTH |  | 347 | 1500 | 26 1/2 | 674 |
| OEC2007 |  | OEC2007-OTH |  | 347 | 2000 | 34 | 862 |

Options

| Product # Kit | Product # Factory installed* | Description | Qty |
| --- | --- | --- | --- |
| KIT-OEC-TR3471 | TRIAC1 | 24V electronic relay: 15A at 347V max. |  |
| KIT-OEC-TR347T1 | TRIACT1 | 24V electronic relay with transformer: 15A at 208V, 240V, 347V |  |

* Pour les options installées en usine, ajouter le numéro de l’option au produit. Voir la section Codification des produits au début du catalogue.

1 Thermostat mural à base tension non inclus.

Ajouter «BL» pour blanc, «AM» pour amande, «AE» pour argent étoilé, «BZ» pour bronze, 
«CM» pour charcoal métallique, «AL» pour aluminium, «NL» pour noir semi-lustré, «SA» pour sable, «SS» pour acier inoxydable. Pour les couleurs AE, BZ, CM, AL, NL et SS les grilles sont peintes en noir.

### Others

| Type | Quantity | Model et description Complementary informations | Volts | Phase | Watts | Length mm/in. | Informations Color/installation |
| --- | --- | --- | --- | --- | --- | --- | --- |

Specifications may change without prior notice

| Project: | Approval Information |
| --- | --- |
| Consultant Engineer: |  |
| Eectrician Contractor: |  |
| Distributor: |  |
| Date: |  |
| Contact in Ouellet: |  |
| Comments: |