Series

OSM-AM	AirMulti Multi-voltage Hand Dryer

Features

Color	-	Standard: white.

Finish	-	Standard: epoxy paint.

Voltage	-	Automatically adjusts itself to all power conditions, from 100V to 240V.

Construction	-	Die cast aluminum housing.

Fan	-	Brush type motor, thermally protected, operating at 7500 rpm.

- Delivers 134 cfm of air volume and 6400 lfm of air velocity (76 dBA with hands).

Heating element	-	Helical coil nickel-chromium alloy wire protected by mica insulator.

Control	-	Automatic infrared sensor.

Installation	-	Surface-mounted with security screws to prevent vandalism (tool supplied).

Warranty	-	2-year warranty against defects.

Application 	-	Ideal for light to medium traffic facilities.

Model

| Product # | Qty | Volts | Watts | Weight |
| --- | --- | --- | --- | --- |
|  |  |  |  | lb | kg |
| OAM1150BL |  | 100 to 240 | 1150 | 10.0 | 4.6 |

# Standard color is white.

### Others

| Type | Quantity | Model et description Complementary information | Volts | Phase | Watts | Length mm/in. | Information Color/installation |
| --- | --- | --- | --- | --- | --- | --- | --- |

Specifications may change without prior notice

| Project: | Approval Information |
| --- | --- |
| Consultant Engineer: |  |
| Electrician Contractor: |  |
| Distributor: |  |
| Date: |  |
| Contact in Ouellet: |  |
| Comments: |